Neural Network Models of Visual Perception with Contour Adaptation

---
Gregory Francis – Contour Adaptation Model - Matlab
- Extension of FACADE (Form-And-Color-And- Depth) “-” interconnected
- Originally developed by Grossberg 1990, with additional stereoscopic vision and object recognition capabilities

---
Model Breakdown
(as described by Francis)
- Two complementary and interacting pathways.
- Combines Feature Contour System (FCS) and Boundary Contour System (BCS) replicating physiological components.
- BCS constrains FCS.
- Contour Adaptation occurs in BCS

---
Boundary Contour System
Gated Dipole Circuit
- Habituating neurotransmitter gate (box) depletes over time (≈ neuron activity)
- Excitation within orientation (↑), Inhibition across orientations (¦)
- Result is dynamic, orientation selective, time dependent representation of boundaries in an image

---
Feature Contour System
Filling-in Domains
- Filling-in typically modeled by diffusion of brightness and color (However the diffusion equation computationally expensive)
- Instead, connected regions are identified across the image from pixels in the immediate surround
- Pixel color and brightness within these connected regions are averaged (“filled in”)

---
Code components
# evaluate function
LGNkernels()
for time in range(t):
     timeCount= timeCount+1
     createStimulus(time)
     LGNcells()
     simpleCell()
     complexCell()
     gateComp(time)
     dipoleComp()
     fillingFIDO()
     saveImages()

---
LGNkernels
Creates 2D Gaussian pulse filters for later use:
- Inhibitory and Excitatory filters (C & E)
- ODOG filters (F)

---
createStimulus
- Input image created, various literature based examples
  condition = “choice”
  e.g. Crosses
- Converted into RGB components
  ”wb” channel used predominately

---
LGNcells
Inhibitory and Excitatory inputs at each pixel produced by convolving “wb” image channel with Inhibitory and Excitatory 2d Gaussian filters. / Centers test gray as zero / Reduces magnitude (inhibitory - smoothes)
Excitatory and Inhibitory inputs are summed into OnOff and OffOn / Interiors of bars magnitudes are altered – edges stay constant / Light bars darken, dark bars lighten
OffOn and OnOff combined and half wave rectified producing positive and negative signals. / Dark bars ignored.. / These are combined to produce output signal of LGN...

---
LGNcells output
Magnitude range of stimuli is reduced. / Edges consist of sharp contrast spikes / Test gray centered at zero

---
simpleCell
LGNcell output signal (image) convolved with Oriented-Difference-of- Offset-Gaussian (ODOG) filters created in LGNcells function

---
complexCell
- 4 Simple cell filter polarities summed into 2 directions
- Threshold set ( maximum = 25 )
- Tonic input added (boost magnitude by +5)
- This represents the
  boundary signal

---
gateComp
- Initiated on first time step
- Produced by manipulating boundary signals
- Boundary signal stronger when adapter present → gate weaker
  “Habituating orientation-specific gates”

---
dipoleComp
- Combines complexCell and gateComp signals with cross orientation weighting
  Sig_h = (gate_h*complex_h) - (W*gate_v*complex_v ), W=0.5
  Sig_v = (gate_v*complex_v) - (W*gate_h*complex_h ), W=0.5
- Half wave rectified and threshold set to 50
- Output of gate dipole circuit:

---
fillingFIDO
- dipoleComp signal summed across orientations, amplified and a threshold set
- Boundary structures used to identify distinct filling in domains.
- A image formed with ISO-numerical regions (FIDOs)

---
fillingFIDO
- Using the initial stimulus as a base, the FIDO image is used to average across uniform regions.
- Producing the output of the code.

---
saveImages
- Save location and image type specified
- Colors horizontal boundaries blue and vertical boundaries green for boundary image.

---
Creating a movie GIF
- From the command line, go to the directory with the images and type:
  convert -quality 100 -dither none -delay 10 -loop 0 All*.png Movie.gif

---
Final Output

---
Limitations
- Not all stimuli match psycho-physical results
- Brightness contrast not explained
- Relatively simple stimuli
- Currently only 2 orientations
- Only works under low contrast conditions (<0.1)

---
Extensions
ISO-orientation surround suppression implementation